## Slide 1: Tidal Power (Ch 5.4, 5.9-5.10)
Phys 105
Dr. Harris
4/1/13

## Slide 2: What Causes Tides?
http://www.pbs.org/wgbh/nova/earth/what-causes-the-tides.html

## Slide 3
high tide
low tide

## Slide 4: History of Tidal
Tidal energy is one of the oldest forms of energy used by humans
Dating back to 787 A.D., tide mills were constructed, consisting of a storage pond and a sluice (gate that controls water flow).
  During the incoming tide (flood), the sluice would open to allow rising waters to fill the storage pond
  During the outgoing tide (ebb), the stored water would be released over a waterwheel
In the early 1960’s, the first commercial scale tidal power plant was built in St. Malo, France, consisting of twenty four 10MW turbines.

## Slide 5: Tidal Barrages
The ocean’s tides can be used to accumulate potential energy, which can be converted to mechanical energy by turning a turbine in a manner quite similar to hydropower.
As the tides rise and fall daily, basins along the shoreline naturally fill and empty. A complete tidal cycle takes 12.5 hours, so there are two high tides and two low tides a day.
Dam-like structures called barrages can be built across the mouths of natural tidal basins with sluice gates. Water can be allowed to rise on one side of the sluice until enough of a hydraulic head is built up to power a turbine.
The turbines are designed to work in either direction to maximize the utilization of the changing tide.

## Slide 6: Tidal Barrages

## Slide 8: Rance River Tidal Power Station
The first commercial tidal power plant in the world is the La Rance Tidal Barrage in France built in 1967.
The average tidal range is 28 ft, with a max of 44 ft. The barrage extends 2500 ft across.
Produces 5.4 GWh of electricity per year, which is only 18% of the available energy in the basin.

## Slide 9: Tidal Turbines
Efforts are underway to anchor turbines to the ocean floor to harness tidal energy. This concept is proven, and in practice in a handful of locations on a small scale.
This form of generation has many advantages over its other tidal energy rivals. The turbines are submerged in the water and are therefore out of sight. They don’t pose a problem for navigation and shipping and require the use of much less material in construction.
Tidal turbines are vastly better than wind turbines in terms of efficiency. A tidal turbine produces 4 times the output power per square meter of sweep area as a wind turbine, with a substantially smaller environmental impact.

## Slide 12: Siemens “SeaGen (S)” Tidal Turbine

## Slide 14: Domestic Tidal Power
There are no tidal power stations in the U.S., but plans are underway to build a small tidal power farm in the East River of NYC.
  300 underwater turbines
  On average, 10 MW of power (44GWh of electricity per year, enough for 8000 households)
Alaska, Maine, and southeast Canada are potential target areas for barrages.

## Slide 15: Ocean Thermal Energy Conversion (OTEC)
The world’s oceans constitute a vast natural reservoir for receiving and storing heat energy from the sun
Nearly 75% of the surface area of Earth is water. Due to the high heat capacity of water, the, water near the surface is maintained at significant higher temperatures than water at greater depth
It is possible to extract energy from the oceans through the use of heat engines in order to exploit the temperature differences between warm surface water and the cold, deep water

## Slide 16: Oceanic Temperature Differences Between Surface and 1000m Depth

## Slide 18: Closed-Cycle OTEC System
Closed-cycle systems have been considered for OTEC.
  In such a system, a low heat capacity working fluid passes through a heat exchanger (evaporator) which
  The vapor passes through an expansion valve and forces the rotation of a turbine
  Cold water from the depths cools the condenses the working fluid via heat exchanger, and the process repeats.

## Slide 20: Example
Using the water temperatures from the last slide, calculate the theoretical efficiency of an ideal heat engine?
Of course, this is the maximum possible efficiency for an ideal system. The actual efficiency would be closer to 3%.
  To produce 40MW, the water intake pipes would need to be 10m in diameter, about the size of a traffic tunnel.
    Average coal plant: 670 MW

## Slide 21: Advancing OTEC?
The OTEC concept was first introduced in 1881. In 1930, the first OTEC test system was constructed.
This test system was open-cycle. Unfortunately, the system consumed more power than it produced.
Very little was done after this until the 1970’s when rising fuel costs prompted the US to reopen studies of OTEC
  The Department of Energy financed the design of a large floating OTEC plant intended to provide power to the islands, with transmission lines running along the ocean floor
  A small test plant (10 kW) was built in the late 70’s and operated successfully for four months off the coast of Hawaii. Since then, there has been no support of OTEC technology

## Slide 23: Wave Energy
The kinetic energy of moving waves can be used to power a turbine.
In this simple example the wave rises into a chamber. The rising water forces the air out of the chamber. The moving air spins a turbine which can turn a generator.
When the wave drops, this creates a vacuum in the chamber, causing air to flow in the opposite direction

## Slide 24: Advantages
Renewable and clean
Tides are predictable
There is a vast potential for energy generation
With tidal turbines, the structures are out of sight
Less required material for tidal turbines than wind

## Slide 25: Disadvantages
Like wind and solar, tidal power is intermittent
  In addition, the hydraulic head obtained from tides is also variable
Tides do not align with peak energy demand times
With regard to barrages, some of the environmental impacts of dams are present with this technology as well, though to a much lower extent
VERY, VERY, VERY EXPENSIVE
  Only produces 1/3 of the electricity that a hydropower plant of equal size would produce
  Wave power sites produce low energy output