## Slide 1: Chapter 2: Atomic Structure & Interatomic Bonding
ISSUES TO ADDRESS...
• What promotes bonding?
• What types of bonds are there?
• What properties are inferred from bonding?

## Slide 2
http://web.mit.edu/newsoffice/2008/adhesive-0218.html
http://robotics.eecs.berkeley.edu/~ronf/Gecko/index.html
Gecko’s toe pads
Extremely large number of microscopically small hairs
gecko-inspired bandage

## Slide 3: Atomic Structure (Freshman Chem.)
atom – electrons – 9.11 x 10-31 kg protons neutrons
atomic number = # of protons in nucleus of atom = # of electrons of neutral species
A [=] atomic mass unit = amu = 1/12 mass of 12C Atomic wt = wt of 6.022 x 1023 molecules or atoms 1 amu/atom = 1g/mol
C 12.011 H 1.008 etc.
} 1.67 x 10-27 kg

## Slide 4: Isotopes
2.2 Chromium has four naturally-occurring isotopes: 4.34% of 50Cr, with an atomic weight of 49.9460 amu, 83.79% of 52Cr, with an atomic weight of 51.9405 amu, 9.50% of 53Cr, with an atomic weight of 52.9407 amu, and 2.37% of 54Cr, with an atomic weight of 53.9389 amu. On the basis of these data, confirm that the average atomic weight of Cr is 51.9963 amu.

## Slide 5: Electric Charge
Atomic Particle
Charge
Mass
Electron
–1.6  10-19 C
9.11  10-31 Kg
Proton
+1.6  10-19 C
1.673  10-27 Kg
Neutron
0
1.675  10-27 Kg
Atomic Model
The coulomb unit is derived from the SI unit ampere for electric current i. Current is the rate dq/dt at which charge moves through a region.

## Slide 6: Atomic Structure
Valence electrons determine all of the following properties
    Chemical
    Electrical
    Thermal
    Optical

## Slide 7: Electronic Structure
Electrons have wavelike and particulate properties.
  This means that electrons are in orbitals defined by a probability.
  Each orbital at discrete energy level is determined by quantum numbers. Quantum # Designation
  n = principal (energy level-shell) K, L, M, N, O (1, 2, 3, etc.)
  l = subsidiary (orbitals) s, p, d, f (0, 1, 2, 3,…, n -1)
  ml = magnetic 1, 3, 5, 7 (-l to +l)
  ms = spin ½, -½

## Slide 8: Electron Energy States
1s
2s
2p
K-shell n = 1
L-shell n = 2
3s
3p
M-shell n = 3
3d
4s
4p
4d
Energy
N-shell n = 4
• have discrete energy states
• tend to occupy lowest available energy state.
Electrons...
Adapted from Fig. 2.4, Callister & Rethwisch 8e.

## Slide 9: SURVEY OF ELEMENTS
• Why? Valence (outer) shell usually not filled completely.
• Most elements: Electron configuration not stable.
Electron configuration
(stable)
...
...
1s
2
2s
2
2p
6
3s
2
3p
6
(stable)
...
1s
2
2s
2
2p
6
3s
2
3p
6
3d
10
4s
2
4p
6
(stable)
Atomic #
18
...
36
Element
1s
1
1
Hydrogen
1s
2
2
Helium
1s
2
2s
1
3
Lithium
1s
2
2s
2
4
Beryllium
1s
2
2s
2
2p
1
5
Boron
1s
2
2s
2
2p
2
6
Carbon
...
1s
2
2s
2
2p
6
(stable)
10
Neon
1s
2
2s
2
2p
6
3s
1
11
Sodium
1s
2
2s
2
2p
6
3s
2
12
Magnesium
1s
2
2s
2
2p
6
3s
2
3p
1
13
Aluminum
...
Argon
...
Krypton
Adapted from Table 2.2, Callister & Rethwisch 8e.

## Slide 10: Electron Configurations
Valence electrons – those in unfilled shells
Filled shells more stable
Valence electrons are most available for bonding and tend to control the chemical properties
  example: C (atomic number = 6)
    1s2 2s2 2p2
valence electrons

## Slide 11: Electronic Configurations
ex: Fe - atomic # =
26
valence
electrons
Adapted from Fig. 2.4, Callister & Rethwisch 8e.
1s
2s
2p
K-shell n = 1
L-shell n = 2
3s
3p
M-shell n = 3
3d
4s
4p
4d
Energy
N-shell n = 4
1s2 2s2 2p6 3s2 3p6
3d 6 4s2

## Slide 12: The Periodic Table
• Columns: Similar Valence Structure
Adapted from Fig. 2.6, Callister & Rethwisch 8e.
Electropositive elements:
Readily give up electrons
to become + ions.
Electronegative elements:
Readily acquire electrons
to become - ions.
give up 1e-
give up 2e-
give up 3e-
inert gases
accept 1e-
accept 2e-
O
Se
Te
Po
At
I
Br
He
Ne
Ar
Kr
Xe
Rn
F
Cl
S
Li
Be
H
Na
Mg
Ba
Cs
Ra
Fr
Ca
K
Sc
Sr
Rb
Y

## Slide 13: Electronegativity
• Ranges from 0.7 to 4.0,
Smaller electronegativity
Larger electronegativity
• Large values: tendency to acquire electrons.
Adapted from Fig. 2.7, Callister & Rethwisch 8e. (Fig. 2.7 is adapted from Linus Pauling, The Nature of the Chemical Bond, 3rd edition, Copyright 1939 and 1940, 3rd edition. Copyright 1960 by Cornell University.

## Slide 14: Ionic bond – metal + nonmetal
donates accepts electrons electrons
Dissimilar electronegativities
ex: MgO Mg 1s2 2s2 2p6 3s2 O 1s2 2s2 2p4
[Ne] 3s2
Mg2+ 1s2 2s2 2p6 O2- 1s2 2s2 2p6
[Ne] [Ne]

## Slide 15: Ionic Bonding
• Occurs between + and - ions.
• Requires electron transfer.
• Large difference in electronegativity required.
• Example: NaCl
Na (metal)
unstable
Cl (nonmetal)
unstable
electron
+
-
Coulombic
Attraction
Na (cation)
stable
Cl (anion)
stable

## Slide 16: Bonding Forces and Energies
The origin of an attractive force FA depends on the particular type of bonding that exists between the two atoms.
Repulsive forces arise from interactions between the negatively charged electron clouds for the two atoms and are important only at small values of r as the outer electron shells of the two atoms begin to overlap.
2.13 Calculate the force of attraction between a K+ and an O2- ion the centers of which are separated by a distance of 1.5 nm.

## Slide 17: Ionic Bonding
Energy – minimum energy most stable
  Energy balance of attractive and repulsive terms
Attractive energy EA
Net energy EN
Repulsive energy ER
Interatomic separation r
r
A
n
r
B
EN = EA + ER =
+
-
Adapted from Fig. 2.8(b), Callister & Rethwisch 8e.

## Slide 18: Examples: Ionic Bonding
• Predominant bonding in Ceramics
Adapted from Fig. 2.7, Callister & Rethwisch 8e. (Fig. 2.7 is adapted from Linus Pauling, The Nature of the Chemical Bond, 3rd edition, Copyright 1939 and 1940, 3rd edition. Copyright 1960 by Cornell University.
Give up electrons
Acquire electrons
NaCl
MgO
CaF
2
CsCl

## Slide 19: Covalent Bonding
C: has 4 valence e-,
needs 4 more
H: has 1 valence e-,
needs 1 more
Electronegativities
are comparable.
Adapted from Fig. 2.10, Callister & Rethwisch 8e.
similar electronegativity  share electrons
bonds determined by valence – s & p orbitals dominate bonding
Example: CH4
shared electrons
from carbon atom
shared electrons
from hydrogen
atoms
H
H
H
H
C
CH
4

## Slide 20
Metallic Bonding
Metallic Bond: -Delocalized as electron cloud
-Non-directional

## Slide 21: Mixed Bonding
Ionic-Covalent Mixed Bonding
% ionic character =
where XA & XB are Pauling electronegativities
%)
100
(
x
Ex: MgO XMg = 1.2 XO = 3.5

## Slide 22: Pauling Electronegativities
For TiO2, XTi = 1.5 and XO = 3.5, and therefore,

## Slide 23: SECONDARY BONDING
Arises from interaction between dipoles
• Permanent dipoles-molecule induced
• Fluctuating dipoles
-general case:
-ex: liquid HCl
-ex: polymer
Adapted from Fig. 2.13, Callister & Rethwisch 8e.
Adapted from Fig. 2.15,
Callister & Rethwisch 8e.
asymmetric electron
clouds
+
-
+
-
secondary
bonding
H
H
H
H
H
2
H
2
secondary
bonding
ex: liquid H
2
H
Cl
H
Cl
secondary
bonding
secondary
bonding
+
-
+
-
secondary bonding
secondary bonding

## Slide 24: Summary: Bonding
Type
Ionic
Covalent
Metallic
Secondary
Bond Energy
Large!
Variable
large-Diamond
small-Bismuth
Variable
large-Tungsten
small-Mercury
smallest
Comments
Nondirectional (ceramics)
Directional
(semiconductors, ceramics
polymer chains)
Nondirectional (metals)
Directional
inter-chain (polymer)
inter-molecular

## Slide 25: Properties From Bonding: Tm
• Bond length, r
• Bond energy, Eo
• Melting Temperature, Tm
Tm is larger if Eo is larger.
r
o
r
Energy
r
larger Tm
smaller Tm
Eo
=
“bond energy”
Energy
r
o
r
unstretched length

## Slide 27
2.20 Make a plot of bonding energy versus melting temperature for the metals listed in Table 2.3. Using this plot, approximate the bonding energy for copper, which has a melting temperature of 1084C.

## Slide 28: Properties From Bonding : a
• Coefficient of thermal expansion, a
• a ~ symmetric at ro
a is larger if Eo is smaller.
=
a
(
T
2
-
T
1
)
D
L
L
o
coeff. thermal expansion
D
L
length,
L
o
unheated, T
1
heated, T
2
r
o
r
smaller a
larger a
Energy
unstretched length
Eo
Eo

## Slide 29: Summary: Primary Bonds
Ceramics
(Ionic & covalent bonding):
Large bond energy
large Tm
large E
small a
Metals
(Metallic bonding):
Variable bond energy
moderate Tm
moderate E
moderate a
Polymers
(Covalent & Secondary):
Directional Properties
Secondary bonding dominates
small Tm
small E
large a
secondary bonding

## Slide 30
Water (Its Volume Expansion Upon Freezing)
https://www.youtube.com/watch?v=4i5r65QGUpw

## Slide 31: Unusual Expansion of Water
Most substances contract upon cooling. But, water expands while cooling from 4 0C until it freezes.

## Slide 32: ANNOUNCEMENTS
Reading: Chapter-2
Self-Assessment Exercise for Chap-2
Homework for Chap-2: 1,4,7,8,14,19.