## Slide 1: Crystal Systems
Unit cell: smallest repetitive volume which contains the complete lattice pattern of a crystal.
Fig. 3.4, Callister & Rethwisch 8e.
a, b, and c are the lattice constants.

## Slide 2: Crystal Structure and Crystal System
Q. What is the difference between crystal structure and crystal system?
A: A crystal structure is described by both the geometry of, and atomic arrangements within, the unit cell, whereas a crystal system is described only in terms of the unit cell geometry. For example, face-centered cubic and body-centered cubic are crystal structures that belong to the cubic crystal system.

## Slide 3: Crystal Systems & Bravais Lattices

## Slide 4: Point Coordinates
Point coordinates for unit cell center are
a/2, b/2, c/2 ½ ½ ½
Point coordinates for unit cell corner are 111
z
x
y
a
b
c
000
111

## Slide 5: Point coordinates for all atom positions for a BCC unit cell

## Slide 6: Crystallographic Directions
1. Vector repositioned (if necessary) to pass
through origin. 2. Read off projections in terms of unit cell dimensions a, b, and c 3. Adjust to smallest integer values 4. Enclose in square brackets, no commas
[uvw]
ex: 1, 0, ½
=> 2, 0, 1
=> [ 201 ]
-1, 1, 1
z
x
Algorithm
where overbar represents a negative index
[ 111 ]
=>
y
Notes: Lecture 2 ended here

## Slide 7: Crystallographic Directions
OA
AO
families of directions <uvw>
All cell edges:
All face diagonals:
All body diagonals:

## Slide 8: Problem 3.32
3.32 Determine the indices for the directions shown in the following cubic unit cell: