Xplorer GLX and Motion sensor	   Name:_______________________

- Instruction sheet:

- Measurement error:

- Measurement check or Calibration:

- Measuring speed/velocity:

- Setup the motion sensor on the lab table and open Position VS. Time graph display.

- Collect data while walking away from the motion sensor, staying at rest for a while, and then walking towards the motion senor.

- Sketch the graph display below, determine the walking speeds, and explain the graph.

E. Pendulum

- Place the motion sensor on the lab-table and set the detector surface perpendicular to the lab-table.

- Set up a simple pendulum so that the bob is at the center of the detector surface.

- Measure the period, T using the stop-watch in the GLX._____________________

- Measure the period using the motion sensor.

  - Figure out which settings (person or cart) works better._____________

  - Observe what happens when the pendulum-bob is too close to the sensor.

  - Measure the period, T using one cycle._______________

  - Measure the period, T by using multiple cycles._____________________

  - Measure the length of the pendulum.

  - Calculate the acceleration due to gravity, g. ( )

http://www.pbs.org/wgbh/nova/galileo/