Position Match with the Xplorer GLX

Topics:

- Software Setup

- Hardware Setup

- Data Collection

- Questions

- Teacher’s Hints

Purpose:

In this experiment, students use the GLX to achieve a kinesthetic understanding of kinematic graphs.

Equipment:

- Xplorer GLX (PS-2002)

- Motion Sensor (PS-2103A)

- Adjustable Angle Clamp (ME-8744)

- Whiteboard - optional

# Experimental Setup

Software Setup

- Turn on the Xplorer GLX .

- Using the USB port, connect the Xplorer GLX to the computer.

- Turn on DataStudio .

- Select the Setup Menu Button  .

(Note: If the above picture does not appear, press “Select Interface” and choose PASPORT. Open the Experiment Setup window again.)

- Double-click the Manage Files icon as in the picture above.

Top of the Document

- Highlight RAM and select Upload To ExplorerGLX…

- Navigate to and open the PositionMatch.glx file.

- Highlight Flash and select Upload To ExplorerGLX…

- Navigate to and open the PositionMatch.glx file.

- Press the Home  button to get to the Home screen.

- Use the arrow and check buttons to navigate to the Data Files Button .

- Select the Position Match file. Press  to open the file as in the picture above.

Top of the Document

- Press the Home  Button then  to observe the graph above.

Hardware Setup

- Connect the Explorer GLX to the Motion Sensor.

- Remove both ends of the Adjustable Angle Clamp.

- Connect one end of the Adjustable Angle Clamp screw to the back of the Xplorer GLX as in the picture above.

Top of the Document

- Connect the bottom of the Motion Sensor to the other end of the Adjustable Angle clamp screw.

- Move the switch at the top of the Motion Sensor to the Stick Figure icon.

Top of the Document

Data Collection Procedure:

- Stand in front of a wall or stand in front of a lab partner holding a whiteboard.

- Observe the Graph.

- Press the Start  Button on the Xplorer GLX.

- Try to match the position-time graph.

- After 11 seconds, press the Stop  Button.

- Press the button and select “Graph 2” as in the picture above.

- The “error” graph will give a score in units of  “m*s.” The lower the score, the better.

- Press the button and select “Graph 1” to return to the original graph.

- Using the arrow and check buttons, navigate to and select the Run number as in the picture above. Delete the data run, if necessary.

- Repeat the previous steps several times and report your best score to your instructor.

Top of the Document

# Questions

- Sketch a velocity-time graph from the position-time graph.

- Sketch an acceleration-time graph from the position-time graph.

- Write a paragraph which describes your motion in the graph. Be as descriptive as possible. Include speeds, directions, positions, etc.

Top of the Document

Teacher's Hints

- Check student setups to make sure the motion sensor points parallel to the floor and that the switch at the top is set to “Person.”

- Make sure that the area around the students is clear of obstacles.

- Tell students that they must hold the Xplorer GLX and Motion Sensor firmly.

- A one to two inch long ¼”x20 bolt and two nuts may be used instead of the Adjustable Angle Clamp. Also, students may just hold the Xplorer GLX securely above the Motion Sensor.